| Data Address | Bit Address | Content | Read write | Address |
| --- | --- | --- | --- | --- |
| 2000H (F1.02=2) | BIT1~BIT0 | 00B：no action 01B：stop 10B：start 11B：JOG start | write | 2000H |
|  | BIT2~BIT3 | 00B：no action 01B：Rev 10B：Fwd 11B：change direction | write |  |
|  | BIT4 | 0B：no action 1B：reset alarm | write |  |
|  | BIT5~BIT15 | reserved |  |  |
| 2001H （F1.01=5） | BIT0~BIT15 | Freq. Command 00000~40000 H3000: 2 digit after decimal point，unit Hz | write | 2001H |
|  |  | Freq. Command 0000~4000 H2000: 1 digit after decimal point，unit Hz |  |  |

| F0.01 | Freq. setting | H3000: 2 digit after decimal point，unit Hz H2000: 1 digit after decimal point，unit Hz | read only | 0001H |
| --- | --- | --- | --- | --- |
| F0.02 | Output freq. |  | read only | 0002H |
| F0.03 | Output current | 1 digit after decimal point， Unit : A | read only | 0003H |
| F0.04 | speed | 0 digit after decimal point， unit : r/min | read only | 0004H |
| F0.09 | output voltage | 1 digit after decimal point， Unit : V | read only | 0009H |
| F0.20 | power | 1 digit after decimal point， Unit : KW | read only | 0014H |
| F0.27 | Alarm code | read only | 001BH |
|  | BIT0 | 1： UC ； 0：no alarm |  |  |
|  | BIT1 | 1： oc ； 0：no alarm |  |  |
|  | BIT2 | 1：communication err.NF ； 0：no alarm |  |  |
|  | BIT3 | 1：output loss phase LO ； 0：no alarm |  |  |
|  | BIT4 | 1：OU ； 0：no alarm |  |  |
|  | BIT5 | reserved |  |  |
|  | BIT6 | 1: LU ； 0：no alarm |  |  |
|  | BIT7 | 1: motor overload OL ； 0：no alarm |  |  |
|  | BIT8 | 1：over torque OT ； 0：no alarm |  |  |
|  | BIT9 | 1：overheat OH ； 0：no alarm |  |  |
|  | BIT10 | 1：no 4-20mA signal ； 0：no alarm |  |  |
|  | BIT11~BIT14 | reserved |  |  |
|  | BIT15 | 1：alarm ； 0：no alarm |  |  |
| F0.28 | BIT0 | 0:fwd 1:rev | read only | 001CH |
|  | BIT1 | 0:stop 1:run |  |  |
| F7.03 | Communication burnout | 0: No treatment 1:Alarm not stop 2:Alarm and stop | write | 02BFH |
| F7.04 | Communication disconnection time setting | 0.0 -100.0 S | write | 02C0H |